## Slide 1: Introduction
Idea of kanban from supermarket.
Kanban Japanese word literally meaning “signboard” or “billboard”
Concept related to lean and just in time production
Kanban is one means through which JIT is achieved

## Slide 2: kanban
Its scheduling system that tells you what to produce when to produce it, and how much to produce
Kanban became an effective tool to support the running of the production system as a whole.
Excellent way for promoting improvements.

## Slide 3: What Kanbans Do
Controls the amounts of raw material amounts and of material in Work in Process.
Smooth’s out flow, if sized properly.
Tells when and where there is a problem in the process.
Assure there is always just enough material on hand to make what is needed.

## Slide 4: Type of Kanbans
Raw Material Kanban-tells suppliers when to send how much of a particular item to a place.
In-Process Kanban-determines the amount of WIP that can be kept between ant two operation in process
Finished Goods Kanban-determines the amount of a product to be kept on hand at any given time. Removal of material from the Finished Goods Kanban acts as a signal for more of that product to be manufactured.

## Slide 5: Types of Kanban Signals
A calculated amount of material kept in a designated space, such as a bin or between lines a workbench or on the floor.
A card that is used to tell the amount of material to be made or ordered.
The markings on a bin that determine when more material needs to be ordered or made.
Any other clear visual signal that indicates it is time to get more material.
.

## Slide 6: How Kanbans work
All of the parts used to manufacture a particular product are identified as well as the number used in each product.
Lead time is calculated, that is the amount of time it takes for the parts to be ordered and delivered.
The demand for the product over a specific length of time is the determinmed.
.

## Slide 7: Work in Process Kanban
First. The process times at each station are calculated
Then, when one station has to take significantly more time to do its wok than previous stations, kanbans are put in to keep material batching to a minimum.
If a station takes twice as long as the station before a kanban half again the size is put in place.
.

## Slide 8: Finished Goods Kanban
The demand for a particular product tracked over time.
Based upon the demand, the safety stock is calculated, that is an amount of product to have on hand to satisfy most orders within a specific window of time.
.

## Slide 9: Thank you